## Slide 1: Wireless Array Based Sensor Relocation in Mobile Sensor Networks
Presented by: Dung T. Nguyen
W. Li, Y. I. Kamil and A. Manikas
Department of Electrical and Electronic Engineering
Imperial College London, UK

## Slide 2
Randomly scattered mobile sensors
Redundant sensors in some area
Coverage holes appear
Move redundant sensors to heal coverage holes

## Slide 3: Outline
Model and Problem statement
Redundant sensor detection
Sensor relocation algorithm
Performance evaluation
Conclusion

## Slide 4: Cooperative sensing model
Each sensor knows its location
Near sensors corporate to form wireless array (WA)
Consider a WA as a big sensor
A redundant sensors lies “inside” another sensor

## Slide 5: Problem statement
Max distance a sensor can move is Lmax
Schedule to move sensors to maximize the coverage area
Approach:
  Detect coverage holes
  Move redundant sensors to heal holes

## Slide 6: Local Detection Diagram
Partition space into areas (cell):
  Each area include 1 sensor
  If a point is cover in an area, it must be covered by the corresponding sensor
Check coverage hole in each cell

## Slide 7: Relocate redundant sensors
Move redundant sensors to cell vertices as many as possible
Broadcast information to neighbor cells to avoid duplication

## Slide 8: Strategies to move sensors
After relocations of redundant sensors, iterative move sensors:
  Rebuild local detection diagram
  Move a sensor to the center of mass of its cell
  Only move sensors if coverage gain is greater than the given threshold
  Stop is there is no movement

## Slide 9: Performance evaluation
Provide better coverage percentage and run in less iteration compared to minimax movement

## Slide 10: Performance evaluation

## Slide 11: Conclusions
Advantages:
  Add redundant sensor detection phase
  Move sensor to the center of mass
  Distributed algorithms
Disadvantages:
  Need to know location information
  Assume wireless array as a big sensor
  When a sensor stops working, many other sensors move to cover its hole

## Slide 12: ZONER: A ZONE-based Sensor Relocation Protocol for Mobile Sensor Networks
Presented by: Dung T. Nguyen
Xu Li and Nicola Santoro
School of Computer Science
Carleton University, Canada

## Slide 13: Problem statement
All sensors are mobile sensor
Each sensor only knows its local topology
When a sensor is failure, find a redundant mobile sensor to replace it

## Slide 14: Coverage hole healing
Each redundant sensor broadcast its locations to all other sensors in a vertical strip
When a sensor fails, its neighbor broadcast the information in a horizontal line
Move a redundant sensor to replace the failed sensor

## Slide 15: Conclusions
Advantages:
  Save energy due to broadcast in a restricted area
  Available set of redundant nodes
  Can work on hybrid sensor networks
Disadvantages:
  No cost optimization
  Simple collision solution
  Each sensor in vertical strips stores too much information

## Slide 16: Conclusions
Improvement (may include in the paper)
  Create set of available mobile sensors in each head node in grid quourum model
  Each head node only stores 4 best mobile sensors in four quad laterals
  Set up the subgraph of head nodes to reduce the number of communication messages.