## Slide 1: Jamming-Aware Traffic Allocation for Multiple-Path Routing Using Portfolio Selection
Authors: P. Tague et al.
IEEE/ACM transactions on Networking
Presented by: Ying Xuan

## Slide 2: Jamming Behaviors
http://khongtenmien.com/forum/showthread.php?p=8462
disturb wireless communications
proactive / reactive
  constant, random, repeat, deceive
  single bit/packet
outsider / insider
static / mobile
nondeterministic and dynamic

## Slide 3: Multiple-Path routing
Anti-jamming techniques = diversity
  Multiple frequency bands
  Different MAC channels
  Multiple Routing paths
Multi-Path Routing
  Each source node chooses multiple paths
  Each path is allocated with different traffic amount (how to avoid congestion?)
  Each path has different probabilities to be jammed (how to measure this?)
Goal: Efficiently allocate the traffic to maximize the overall throughput.
http://w3.antd.nist.gov/adhoc/Project_drouting.shtml

## Slide 4: Roadmap
Use PDR to approximate the overall throughput
  What is PDR? How to get PDR?
Use a quadratic program based on Portfolio Selection Theory to give the optimal solution
  Objective Function? Constraints?
Use Lagrangian dual decomposition to get a distributed solution
  Efficiency: accuracy, convergence, scalability.

## Slide 5: Represent the throughput - I Estimate local packet success rates (LPSR)
Each node updates (LPSR), Update period T << Ts update relay period
Estimated value by Packet Delivery Rate (PDR)
Variance by the variance of PDR

## Slide 6: Represent the throughput - II End-to-End Packet Success Rate
Mean
Variance/covariance
Given that there are Ls paths at source node s, what does these two above mean?

## Slide 7: Represent the throughput – III
Given that the traffic allocation vector at node s is
  Expected throughput:
  Variance:

## Slide 8: Formulate Optimal Solution – I Portfolio Selection
Analogy of concepts
http://proteger.com.my/articles/investment/modernportfolio.html

## Slide 9: Formulate Optimal Solution – I Portfolio Selection (cont’)
risk-aversion factor ks
  ks = 0 means the throughput is maximized regardless of any risks
  Ks>0 (0.005 in the simulation)

## Slide 10: Formulate Optimal Solution – II Congestion Avoidance
Delivery rate from s to node i is
The aggregate traffic going through link (i,j) is

## Slide 11: Formulate Optimal Solution - III

## Slide 12: Iterative and Distributed Solution
Many allocation quadratic program on large-scale networks can be solved efficiently through decomposition techniques
Daniel P. Palomar and Mung Chiang, A Tutorial on Decomposition Methods for Network Utility Maximization.
Lagrangian dual decomposition

## Slide 13: Lagrangian Duality

## Slide 14: Decomposition Topology

## Slide 15: Decomposition Flow
decouple(c)
lagrangian
dual function
the dual function could be solved using a gradient method

## Slide 16: Apply to this formulation
Local update at step 3 requires mutual information exchanges at all the sources……

## Slide 17: What can we learn
Way to formulate throughput
Way to solve quadratic program distributedly for large-scale networks

## Slide 18: Q&A
Thanks!