## Slide 1: Flutes vs. Cellos: Analyzing Mobility-Traffic Correlations in Large WLAN Traces
Babak Alipour*, Leonardo Tonetto, Aaron Yi Ding, Roozbeh Ketabi, Jörg Ott, Ahmed Helmy
Computer and Information Science and Engineering,
University of Florida (UF)
Department of Informatics,
Technical University of Munich (TUM)
This talk was presented at INFOCOM 2018
Notes: Babak Alipour (babak.ap@ufl.edu, babak.alipour@gmail.com) is the presenter of these slides at IEEE InfoCom 2018. He is PhD student at University of Florida, supervised by Prof. Ahmed Helmy (helmy@ufl.edu).
Tech report of this publication can be found at https://arxiv.org/abs/1801.02705
* This is the result of 4 years of efforts and collaboration between UF and TUM, with this work as a stepping stone for future integrated mobility-traffic models.
* Big data used here is 30TB in size.

## Slide 2: Outline
Introduction: Motivation, Framework
Datasets & Device Classification
Mobility Analysis
Traffic Analysis
Integrated Analysis
Conclusion

## Slide 3
Two major factors affecting mobile network performance are:
      mobility and network traffic patterns and models.
Simulation, analysis, and prediction schemes rely on such models.
Earlier mobility modeling studies use pre-smartphone WLAN traces.
Mobility-Traffic Interdependence not well-studied:
    Earlier models designed independently
    No integrated mobility-traffic models exist!*
Motivation
Notes: Mobility & Traffic Aspect/Dimension/Plane
Several datasets can be found in CRAWDAD [https://crawdad.org/] and MobiLib [https://www.cise.ufl.edu/~helmy/MobiLib.htm]
* There is also a scarcity of publicly available datasets containing both dimensions.
* Mobility, Network usage, and device type characterize different aspects of human behavior.

## Slide 4
(I) How different are mobility and traffic features across:
    device types – time – space ?
(II) What are the correlations between these features?
(III) Should new integrated mobility-traffic models be devised to capture the differences?
    What is the value/utility of integrating mobility and traffic?
Goals
Notes: Goal I) It’s about finding the trends.
Goal II) It’s necessary to answer goal III.
The main goal of this study is to provide the foundation for an integrated mobility-traffic model.

## Slide 5: Flute vs Cello Mobility
Captures ‘on-the-go’ usage scenarios (i.e., smartphones)
Higher mobility expected, needs to be quantified
Traffic patterns?
Captures ‘sit-to-use’ usage scenarios (i.e., laptops)
Lower mobility expected, needs to be quantified
Traffic patterns?
Flutes
Cellos
Comparison not well-studied
Goal I) How different are mobility and traffic characteristics across device types, time and space?

## Slide 6
Cello ‘Mobility’*!!
* We thank Prof. Mostafa Ammar for suggesting the term ’cello mobility’

## Slide 7
Cellos , Laptops = sit-to-use
Flutes, Smartphones = use-on-the-go
Flutes vs Cellos:

## Slide 8: Framework (Abstract)
Data
WLAN Traces
NetFlow
Analysis
Cellos vs Flutes
Spatio-Temporal Characteristics
Modeling
Mobility & Traffic feature extraction
Correlations
Device Classes
DHCP
Core (merged)
Traffic and Mobility Features
Mixture Models and Synthesis
Notes: Let’s walk through the framework from the data, through analysis and all the way to modeling insights.

## Slide 9
Framework
(detailed)
(Framework for Large-scale Analysis of the Mobile
Society)
FLAMeS System Overview
Notes: 3 Layers, the first layer has 3 parts (a, b, c)

## Slide 10
Framework
FLAMeS Framework
Goal I) Get device type, time and space features
Goal II) Analyze relationships
Goal III) Quantify the value of integrated model
Multi-sourced data, Modular design, to address our goals of:

## Slide 11: Outline
Introduction
Datasets & Device Classification
  WLAN
  NetFlow
  DHCP and Core
  Auxiliary Datasets
Mobility Analysis
...

## Slide 12
FLAMeS Framework
Datasets
Goal I) Get device type, time and space features

## Slide 13: Datasets (WLAN, NetFlow, Aux.)
WLAN
  555M records (association/authentication events)
  Includes: user MAC, AP MAC & Name, IP address, timestamp.
  1760 access points in 138 buildings over 479 days (2011-2012).
  316k devices.
  AP name embeds location information.
    Building, floor and room numbers.
    Google Maps API used to fetch latitude/longitude*.
Building Room
Floor
Notes: Datasets comes from APs located on University of Florida campus.
* We fetched 8000 mapped APs around the campus area from a crowd-sourced service, wigle.net.
For the 130 matched APs in 42% of buildings (i.e., 58 bldgs), all were less than 200m from their mapped location; an error of less than 1.5% of the campus area. This is very reasonable for our study purposes.

## Slide 14: Datasets (WLAN, NetFlow, Aux.)
NetFlow
  76 Billion records (30TB in size*), 80k devices.
  Includes source/destination IP addresses and port numbers, protocol, packet count, size, and duration.
  Same wireless network (University of Florida campus), April 2012.
NetFlow sample data
Notes: * In plain text, raw, uncompressed format. Very compressible.

## Slide 15: Datasets (WLAN, NetFlow, Aux.)
    Reverse DNS (*)
    Device type survey
    University buildings listing
    Google Maps API
    Crowd-sourced wigle.net data
Used for device type classification
Used for location verification
Notes: * https://scans.io/study/sonar.rdns, MIT-license

## Slide 16
Device-type Classification Flowchart
Overall: 97% of devices in NetFlow labeled (~50k flutes, ~27k cellos) *
00:D0:B7 # Intel Corporation
00:D0:B7:01:02:03 User MAC
Cello**
Notes: Using a survey of MAC prefixes, we find the manufacturer. Otherwise, we use ‘mobile’ domains, which are the domains typically used when a browser with a mobile device agent is detected.
* Out of ~80K devices in NetFlow/Core dataset.
** We are not aware of any Intel-branded flutes during the collection duration of the WLAN dataset.

## Slide 17
Time series for 25 days of combined WLAN-NetFlow traces after preprocessing and sanitation of datasets
Notes: We’re done with preprocessing and sanitation of datasets.

## Slide 18
(I) How different are mobility and traffic features across:
    device types – time – space ?
(II) What are the correlations between these features?
(III) Should new integrated mobility-traffic models be devised to capture the differences?
    What is the value/utility of integrating mobility and traffic?
Goals
But what are the characteristics of mobility and traffic dimensions?

## Slide 19
FLAMeS Framework
Data cube, traffic/mobility analyzed temporally, spatially, and per device type
Goal II) Analyze relationships/correlations of this data cube
Notes: We’re done with preprocessing and sanitation of datasets, let’s move on to analysis of this data cube.

## Slide 20: Outline
Introduction
Datasets & Device Classification
Mobility Analysis
  Features
  Results
Traffic Analysis
...

## Slide 21: Mobility
Choose mobility features that capture human movement patterns:
  Session start probability
  Radius of gyration
  Visitation preferences and interests
  Session duration per building
  Hourly associations
  Return probability …
Analyze these features independently, before integration with traffic.
Notes: The selected list of features was chosen to capture human mobility patterns, based on exploratory analysis and prior literature.
Several other features that were highly correlated (>0.9 Pearson’s r) were removed.

## Slide 22
Break
  Session start probability
Spikes match periodic classes (strongest: Cellos in academic bldgs.)
Significant drop after 5pm for Cellos in academic and social.
Reversal of prob. after 5pm in academic, social and library.
Class
Notes: Please note that the most significant spikes are in academic buildings, where most of the devices starting sessions during class hours are Cellos.

## Slide 23
  Return probability
Returning spikes at every 24 hours, with the highest peaks at 48 and 168 hours (2 and 7 days, corresponds to schedule of classes, Tuesday/Thursday or Monday/Wednesday/Friday)
No significant difference between flutes and cellos.
MWF
Tue,Th
1 week
Notes: RW: Random Walk
This metric captures intra-semester periods. Surprisingly, the highest spike is at 2 days.
This is in contrast to some other related studies that found the highest spike on 24 hours.
Class schedules are usually Tuesdays/Thursdays (2 days apart) or Monday/Wednesday/Friday (again 2 days apart).
Flutes and cellos show similar behavior in terms of return probability

## Slide 24: Mobility Analysis Summary
Quantified features: jumps, radius of gyration, number of APs visited,…
Flutes:
    have higher overall mobility – likely in social and housing bldg.
Cellos
    visit fewer places – likely in academic bldg. – some active in weekends.
Different behaviors on weekdays vs. weekends.
Similar pattern of return probability (peaks at 2 & 7 days).

## Slide 25
Weekday
Weekend
Summary of
Mobility Features
LJM: maximum jump [m]
DIA: diameter [m]
TJM: total trajectory length [m]
GYR: radius of gyration [m]
BLD: no. uniq. buildings
APC: no. uniq. APs
PDT: time spent at preferred building [min]
DLT: total session time at each building [s].
Up to 3 orders of magnitude difference between Cellos and Flutes

## Slide 26: Outline
Introduction
Datasets & Device Classification
Mobility Analysis
Traffic Analysis
Integrated Mobility-Traffic analysis
Conclusion

## Slide 27: Flow-level statistical characterization
  Flute flows are 2x larger on average (more packets and larger packets).
  Flow sizes follow a lognormal distribution*:
Flow sizes
Lognormal fit
Notes: * Lognormal fit for flow sizes has been shown in the research before [1], and was verified on our dataset.
[1] “On the log-normal distribution of network traffic”, Antoniou, I and Ivanov, Victor V and Ivanov, Valery V and Zrelov, PV 2002
* Lognormal fits for the two device types have very different parameters.

## Slide 28: Network-centric (spatial) analysis
MB per day, log-scale
Cellos consume more traffic!
Much higher traffic consumption on weekdays!
Although flute flows are bigger, there are fewer of them  Overall, flutes consume less data.
Weekends
Weekdays

## Slide 29: User-centric (temporal) analysis
Active time (minutes per day)
Cellos have 4x average active time compared to flutes.
Active time of cellos increases on weekends. (fewer devices, but more active)
Flutes are more bursty.
Flutes
(smartphones)
Cellos
(laptops)
Notes: Joke: Graduate students on weekends with their cellos!?

## Slide 30: Traffic Analysis Summary
Flutes:
  More bursty, with bigger flows and lower active duration
  Potential causes: Intermittent usage, bundling of requests to save battery.
Cellos consume more (higher overall traffic volume, packet rate, etc.)
Different behaviors on weekday and weekends.
Separation of device types & weekday/weekend across both Mobility and Traffic planes is important for planning, modeling and simulation.

## Slide 31
Summary of
Network Traffic Features
Weekday
Weekend
Total flow bytes
Avg. flow bytes
Std. flow bytes
Total active time
Avg. active time
Total flow count
Std. flow counts
UDP bytes / total bytes
UDP flows / total flows
Avg. IAT
Std. IAT
Up to 2 orders of magnitude difference between Cellos and Flutes

## Slide 32: Outline
Introduction
Datasets & Device Classification
Mobility Analysis
Traffic Analysis
Integrated Mobility-Traffic Analysis
Conclusion

## Slide 33
(I) How different are mobility and traffic features across:
    device types – time – space ?
(II) What are the correlations between these features?
(III) Should new integrated mobility-traffic models be devised to capture the differences?
    What is the value/utility of integrating mobility and traffic?
Goals
Notes: Goal I) It’s about finding the trends.
Goal II) It’s necessary to answer goal III.
The main goal of this study is to provide the foundation for an integrated mobility-traffic model.

## Slide 34
FLAMeS Framework
Goal III) Should new models be devised? What is the value and utility of an integrated model?

## Slide 35: INTEGRATED MOBILITY-TRAFFIC ANALYSIS
Why?
  Mobility, Network usage, and device type characterize different aspects of human behavior.
  They are usually studied independently, but they are correlated.
  Need to quantify and model relationships among these features.
How?
  Feature engineering
  Statistical distribution fitting and machine learning

## Slide 36: INTEGRATED MOBILITY-TRAFFIC ANALYSIS
Feature engineering
  Mobility
  Traffic
  Cross-dimension
Modeling insights

## Slide 37: Feature engineering : Mobility
Correlation-based feature selection (CFS)
Selected features are:
  DLT: Delta time between network associations
  DIA: Diameter of mobility
  TJM: Total (sum) jumps
  PDT: Delta time at preferred bldg.
  APC: Unique AP count
Correlation plot of mobility features*
Weekday
Weekend
Cello
Flute
Weekday
Weekend
Notes: * The top triangle corresponds to weekdays, and the bottom is for weekends. Each cell’s right half is for Cellos, and left half is for Flutes.
* Features which were >0.9 correlated with the any of the presented features were removed.
* These features are calculated for each user, over a week.
* The correlation plot for mobility had an error (reversed Y-axis) that has since been fixed in the slides and arXiv tech report.
* For example, the correlation between DLT and PDT is high on weekends and low on weekdays. This is because users do not have many short duration associations on weekends and spend most of their time at their preferred bldgs.

## Slide 38: Feature engineering : Traffic
Selected features are:
  TBY: Total flow bytes
  ABY: Avg. flow bytes
  SBY: Std. flow bytes
  TAT: Total active time
  AAT: Avg. active time
  TFC: Total flow count
  SFC: Std. flow count
  RUB: ratio of UDP bytes to total
  RUF: ratio of UDP flows to total
  AIT: Avg. IAT
  SIT: Std. IAT
Correlation plot of features*
Weekday
Weekend
On weekends, Lower for Cellos, Higher for Flutes
Cello
Flute
Higher on weekends
Notes: Each cell’s left half is for flutes and right half is for cellos, the upper right triangle is for weekdays and the lower left for weekends.
Features which were >0.9 correlated with the any of the presented features were removed.

## Slide 39
Correlation of mobility vs. traffic on weekdays (top) vs. weekends (bottom) for flutes (left) and cellos (right).
Flute - Weekday
Flute - Weekend
Cello - Weekday
Cello - Weekend
Traffic
Mobility
Feature engineering : Cross-dimension
Notes: Mobility vs Traffic features for (Flutes/Cellos, Weekday/Weekend)
There are currently no existing models that capture these correlations, that can be crucial in many applications including prediction, caching, resource allocation, among others. They are modeled independently, but correlations matter, and they help in modeling.
​There are more details and explanation in the paper.

## Slide 40: INTEGRATED MOBILITY-TRAFFIC ANALYSIS
Feature engineering
  Mobility
  Traffic
  Cross-dimension
Modeling insights
  Goal III) What is the value and utility of an integrated model?
  Generative modeling

## Slide 41
Modeling Insights
Capture mobility and traffic features, while maintaining relationships among them.
Goal III) What is the value / utility of an integrated model?
Improve accuracy of existing algorithms and applications by revealing cross-dimension features.
Provide a modular, systematic architecture that is extensible and customizable.
Allow modeling of device types, such as flutes, cellos, and a spectrum of devices.
Notes: * Skip if short on time.

## Slide 42: Modeling Insights
Goal III) What is the utility of an integrated model?
Can we classify devices using their mobility and/or traffic features?
Chart: Accuracy (%)
 | 65
 | 79
 | 81
 | 86
Mobility alone
Traffic alone
Combined
Combined, weekday/weekend separated
32% increase in accuracy!
Notes: SVM classifier. 5-fold Cross-Validation. Using default parameters.

## Slide 43: Modeling insights
  Generative modeling
    Various uses in simulation, benchmarking, planning and more.
    Based on spatio-temporal features in mobility, traffic, device type
    Capture interdependence of features
    Privacy preserving*
  Gaussian Mixture Model (GMM)
    Mobility features
    Traffic features
    Combined Mobility-Traffic features
Notes: * This is an important future direction for synthesizing data points.

## Slide 44: Modeling insights
Gaussian Mixture Model (GMM)
Using Kolmogorov–Smirnov (KS) test to compare synthetic vs original
* Average KS statistic (lower is better).
* Weekday only.
 | Test on Mobility |  | Test on Traffic | 
Train on Mobility | 0.117 | 0.194 | N/A | N/A
Train on Traffic | N/A | N/A | 0.179 | 0.139
Train on Combined | 0.088 | 0.170 | 0.176 | 0.139
Cello
Flute
25% reduction in error for Mobility!
Notes: Similar patterns on weekends were observed (not presented here for brevity).
The parameters of the GMM are the same for the entire table.
​The improvement is likely to increase by using different generative models, which is a work in progress.

## Slide 45: Next steps?
Investigation of services and relationship of user interests with spatio-temporal characteristics of mobility and traffic.
Expand device type classification, for example, smartphones vs tablets – do we have “guitars” as well?!
Studying datasets from other network settings and environments to further validate the observed behaviors
Examining the minimum number of parameters required (parsimonious model) to approximate user behavior within given error bounds
Notes: * Skip if short on time.

## Slide 46
Framework
FLAMeS Framework
Goal I) Get device type, time and space features
Goal II) Analyze relationships
Goal III) Quantify the value of integrated model
Goal I) Get datasets from various environments
Future Framework
Goal II) Analyze minimum number of parameters for a parsimonious model, expand the cube if necessary
Goal III) Investigate services, measure and validate accuracy of generative models
Notes: Animated slide.

## Slide 47: Takeaways
It is crucial to differentiate flutes vs. cellos
  for both mobility and traffic.
  Correlations of these features matter, and should be captured in models!
There is significant potential for integrated mobility-traffic models that capture relationships across device types, time and space.

## Slide 48: Thanks! Questions?
Do you have mobility/traffic datasets? Please let us know 
Babak Alipour babak.ap@ufl.edu, Ahmed Helmy helmy@ufl.edu
Parts of materials will be shared for reproducibility!
Link: cise.ufl.edu/~helmy/MobiLib.htm
Look for Flutes vs. Cellos!
Flutes vs. Cellos: Analyzing Mobility-Traffic Correlations in Large WLAN Traces
Notes: Work in progress!
Do you have mobility/traffic datasets? Please let us know 
Tech report of this publication can be found at https://arxiv.org/abs/1801.02705

## Slide 49: Acknowledgements:
We thank Dr. Alin Dobra for help in the computing cluster, and the anonymous reviewers for useful feedback.
Dr. Mostafa Ammar suggested the term ’cello mobility’.
Partial funding was provided by NSF 1320694 at Univ. of Florida, August-Wilhelm Sheer fellowship at Technical University-Munich, and Aalto Univ.
Several pictures in the slides from retrieved from https://pixabay.com

## Slide 50: Backup Slides

## Slide 51
Scarcity of publicly available datasets containing both dimensions
  Limitations of available datasets and scenarios in time & space
Multi-dimensional comparative analysis
  Identifying mobility/network traffic features
  Device type categorization
This is the result of 4 years of efforts, with this work as a stepping stone for future integrated mobility-traffic models.
Challenges

## Slide 52
Privacy concerns are another important challenge.
An integrated mobility-traffic model should be able to provide synthesized data points that capture the statistical characteristics of data for various applications, without exposing the original data points, and subsequently the users’ privacy.
One of the purposes of our model to have the ability to create ‘virtual campuses’, with adjustable features while also maintaining the relationships among features.
Challenges

## Slide 53: Datasets
DHCP
  DHCP logs derived from WLAN events.
A DHCP lease record would indicate: user , AP , IP , t1, t2
  i.e. User , was at AP , associated with IP from t1 to t2.
Wireless association logs for a device at different times
DHCP record 1
Duration = t2-t1

## Slide 54: Datasets
Core
  Merge DHCP and NetFlow to capture mobility AND traffic.
  Enables analysis of flows in different locations (spatial analysis)
  For a DHCP lease session LS, all flows whose source or destination IP address is the same as the lease, and whose entire lifetime falls within the lease duration, are associated with LS to produce the Core dataset of this study.
  i.e. match on src IP / dst IP, and timestamps.

## Slide 55: Datasets
NetFlow (top) and AP logs/DHCP (bottom) sample data
Bldg
Flr
Rm
Match any?
Unique user ID
Contained in?
 Resulting core dataset contains mobility and traffic information!
Notes: Due to the massive size of the NetFlow, this join query takes several days .

## Slide 56: Device type classification
Two heuristics:
  Device type survey*
    MAC prefixes (OUI), some manufacturers only produce flutes or cellos.
    Labels 46% of devices
  NetFlow + Reverse DNS
    Find websites mostly serving labeled flutes (e.g. admob.com)
    Verify with survey above (92% accuracy**)
    Extend classification using OUI of devices contacting such websites
Overall: 97% of devices in NetFlow labeled (~50k flutes, ~27k cellos) ***
Notes: * We utilized a survey done by our lab under supervision of Prof. Ahmed Helmy.
** Looking solely at the intersection of devices already classified using the survey and admob.com users, 92% are flutes.
*** Out of ~80K devices in NetFlow/Core dataset.

## Slide 57
Standard deviation of user’s movements and its center of mass (centroid of all movements)
Illustration of Radius of gyration and diameter mobility features
  Radius of Gyration (GYR)
Notes: Where is the distance between a user’s logged location and center of mass.
Where 𝑟_𝑖−𝑟_𝑐𝑚is the distance between a user’s logged location and center of mass.

## Slide 58
  Radius of gyration
After an initial transient period of about one week, this value stabilizes even across different semesters.
For a random walk, radius of gyration keeps increasing.

## Slide 59
  Radius of Gyration (GYR)
Stable after initial transient period of ~1 week, even across semesters (not shown)
Substantial drop for cellos on weekends.
Some flutes show higher radius on weekends.
Despite large campus (8.1km2), area of activity is limited. (more pronounced for Cellos)
Flutes
Cellos

## Slide 60
  Visitation preferences and interests
Required time t to visit S(t) locations.
After an initial exploration period of one week the rates of new visits change similarly for both device types, and new exploration rates show up at 120 and 240 days (~120 days is the usual length of a semester).
Fig. 4 (b) Visited locations S(t).
Vertical lines at 7, 120 and 240 days.
Notes: This metric captures inter-semester behavior.

## Slide 61
  Visitation preferences and interests
The probability of finding a device at its L-th most visited location.
Similar patterns, but different coefficients for flutes vs cellos
Zipf’s plot on L visited access points for L = 20,25,30,35.

## Slide 62
  Session duration per building
Knees at 1 and 2 hours at academic bldgs. (correspond to classes) .
Flutes and cellos present certain similarities in their usage, such as during classes
Different building categories show differences. (e.g. Higher probability of long sessions in libraries)
Probability P (t) of session duration t. The scale of all axes in smaller inner plots are the same as their parent plot.

## Slide 63
  Hourly associations
The majority of devices appear online between 9am and 8pm.
More Flutes likely early morning.
More Cellos likely midday.
More Flutes likely late evening.

## Slide 64
  Hourly associations
The majority of devices appear online between 9am and 8pm.
More Flutes likely early morning.
More Cellos likely midday.
More Flutes likely late evening.
Notes: 2 reversals of the device percentages to associate with WLAN happen at 9 AM and 7 PM.

## Slide 65
  Visitation preferences and interests
academic, police and museum buildings tend to have laptops staying longer.
social and housing buildings, there is a higher probability of having flutes staying longer.
Notes: * Each dot represents median time for a given location.

## Slide 66
Weekday
Weekend
Mobility Features

## Slide 67: Traffic
  Flow-level statistics
    Analyze features of individual users
    Important for verification of synthetic data points*
  Network-centric (spatial) analysis
    Analyze load characteristics from the network viewpoint
  User-centric (temporal) analysis
    Analyze user behavior over time
Notes: * An integrated mobility-traffic model should encapsulate statistical characteristics of each dimension (mobility/traffic).

## Slide 68: Flow-level statistical characterization
  Flow Inter-arrival time (IAT) is 1.8x higher for flutes.
  Flow IAT follows a beta distribution
    High estimated kurtosis and skewness hints at infrequent extreme values. Flutes face more extreme periods of inactivity overall.
Notes: * Beta fits for the two device types have different parameters.

## Slide 69: Flow-level statistical characterization
  Most flows are short-lived
    Average <2s
    Median 64ms for Cellos
    Median 128ms for Flutes
  Prevalence of TCP is much higher in flutes (98.2% vs 78.5% of flows).

## Slide 70: Network-centric (spatial) analysis
Why?
  Gain insight from viewpoint of the network
  Analyze load at different APs for planning
  Compare and contrast buildings
How?
  Calculate flow metrics for each AP and aggregates per building over weekdays & weekends
Notes: I will only provide a sneak peak of the spatial (and later temporal) analysis.

## Slide 71: Network-centric (spatial) analysis
On weekends:
  60% of APs see no flute flows and 70% receive no cello flows.
  At least one AP in >80% of buildings sees traffic*.
  Traffic is clustered in a few areas (APs) of of each building.
  Average traffic consumption and packet rate are half of weekdays.
  Median traffic consumption drops to near zero for flutes.
    Most flutes just ‘pass-by’.
Notes: * This means that while most APs do not see traffic, most buildings do have traffic!  traffic is clustered in a few areas of each building!

## Slide 72: User-centric (temporal) analysis
Why?
  Gain insight from behavior of users
  Analyze user patterns for modeling
How?
  Calculate flow metrics aggregates for each user separately

## Slide 73: User-centric (temporal) analysis
Traffic Consumption (MBs per day)
90% of cellos consume < 700MB, for flutes < 200MB
Median traffic consumption of flutes is near zero on weekends. Whereas remaining cellos consume more.
Flutes
Cellos

## Slide 74
Network Traffic Features
Weekday
Weekend

## Slide 75: Modeling Insights
Can we classify devices using their mobility and/or traffic features?
Accuracy:
  Mobility alone  65%
  Traffic alone  79%
  Mobility and traffic  81%
  Mobility and traffic, separate features for weekdays/weekends  86%
Users’ behavior (both flutes and cellos) is more distinguishable with combined mobility and traffic features; especially when temporal features such as weekdays are considered separately from weekends.
( than either mobility or traffic alone)
Chart: 
 | 65
 | 79
 | 81
 | 86
Notes: SVM classifier. 5-fold Cross-Validation. Using default parameters.

## Slide 76: Modeling insights
Gaussian Mixture Model (GMM):
  Combined Mobility-Traffic features  Average KS statistic of all features is 0.15 for flutes and 0.14 for cellos.
  Importantly, the combined model produces samples whose mobility or traffic features match the original data better, compared with training a GMM on mobility or traffic features alone (based on KS statistic).

## Slide 77: Next steps? continued
Flutes and cellos are likely two points in a dimension that is continuously changing:
  Differentiation in device classes appear, for example, smartphones vs tablets – do we have “guitars” as well!? (Prof. Jörg Ott suggested the ‘guitar’ category.)
  New devices such as fitness trackers, smart watches, glasses, etc.
  New form factors for smartphones/tablets could blur the line again.

## Slide 78: Conclusion
AP associations allow us to calibrate user mobility and determine their community structures (and “hotspots”), while daily and weekly activity patterns help outline user schedules—which could be parameterized.
Traffic flows per device can be created from our corresponding distributions, while AP traffic observations allow parameterizing the above “hotspots” with respect to user activity.
This could form a basis for generating parameters for established mobility models, possibly extend them as needed, and augment them with adequate correlated traffic models.

## Slide 79: Conclusion
It is crucial to differentiate flutes vs. cellos for both mobility and traffic due to their very different nature. Correlations of these features matter, and should be captured in models!
Traffic generation, spatial locations, and temporal behavior can be linked per device type and per user “community” (e.g., students of different disciplines at various buildings).
There is significant potential for integrated mobility-traffic models that capture relationships across device types, time and space.