## Slide 1: Geocast DTNs
Presented by: Khulood Azwary
Kratika Gupta

## Slide 2: A General Overview
Geocast deals with sending of the messages to a node in a specific geographic region.
Various protocols have been proposed over the years employing various methods for the same.
  Eg Greedy algorithm, zones/clustering, planarization in case of local maxima

## Slide 3: GeoDTN+Nav: Geographic DTN Routing with Navigator Prediction for Urban Vehicular Environments
Pei-Chun Cheng · Kevin C. Lee · Mario Gerla · Jérôme Härri

## Slide 4: GeoDTN+Nav
It is hybrid of greedy algorithm and perimeter mode and DTN in case it face partitioned network

## Slide 5: GeoDTN+Nav
GPSR: Greedy Perimeter Stateless Routing .
GPCR: Greedy Perimeter Coordinator Routing.
Both use greedy algorithm to forward packets by selecting relays with the best progress toward the destination and recovery mode in such solution fail.
In recovery mode “local maximum” they use planarization and forward packet around the obstacle.

## Slide 6: GeoDTN+Nav
It is complex and force a packet
to progress in small steps.
Routing loop in high mobility.
Increase latency.
Inability to to deliver packets
across partitions in case of
partitioned network.
However, DTN can forward packets through partition

## Slide 7: GeoDTN+Nav
Virtual navigation interface framework:
They classify vehicles based on traffic pattern.
Retrieving rout-info and confidence from vehicles.

## Slide 8: GeoDTN+Nav
Switch score is calculated for each neighbor.
It’s combined of three factors: P(h),Q(Ni),Dir(Ni).

## Slide 9: Switching from DTN to Greedy Mode

## Slide 10: Synthetic topology

## Slide 13: GeoDTN+Nav
Strengthens:
Using real traces from Intelligent Driver Model with Intersection Management (IDM-IM) by VanetMobiSim.
Inventing VNI (Virtual navigation interface )Framework.

## Slide 14: GeoDTN+Nav
Weakness:
In addition to planarization weakness also it relies in mobility in DTN phase.
Doesn’t use of useful links between tow nodes on different roads.
Switching to greedy mode depends on distance between the initial local maximum node and destination.
Moving destination
Privacy issue.

## Slide 15: A Novel Geocast Technique with Hole Detection in Underwater Sensor Network
Sanjay K. Dhurandher
Mohammad S. Obaidat
Megha Gupta

## Slide 16: A Novel Geocast Technique with Hole Detection in Underwater Sensor Network
It consists of six parts:
Neighbor Table Formation Algorithm
Route Discovery Algorithm
Route Maintenance Algorithm
Multicast Tree Formation for routing in geocast region
Hole Detection in geocast region
Boundary routing around the geocast region.

## Slide 20
Weakness:
Overhead in first 2 algorithm part.
Doesn’t clear how to determine r in virtual area.
Scalability.

## Slide 21: DTFR: A Geographic Routing Protocol for Wireless Delay Tolerant Networks
Anna Sidera, Stavros Toumpis

## Slide 22: Routing
Sender sends the packet to a location known as Firework Center in geocast region according to past information (location and mobility pattern)

## Slide 23
Works in 4 phases:
  Homing Phase
  Explosion Phase
  Spread Phase
  Lock Phase

## Slide 24
Homing Phase
Greedy strategy used
Packet is forwarded as long as nodes are found closer to Firework Center
If no suitable node found, current holder of packet waits for one to emerge
Explosion Phase
Starts when packet reaches FC
A number of replicas of the packet are created

## Slide 25
Spread Phase
Replicas are forwarded in various directions inside the geocast region to ensure delivery to destination
Firework Endpoints are also determined
Lock Phase
Starts when a known route to destination is encountered
This pre-calculated route is then used to send the packet to destination

## Slide 26: Priority of Phases over the Other
Lock Phase > Homing Phase > Explosion Phase > Spread Phase

## Slide 29: Weaknesses
Large number of nodes: This is not possible always.
During Homing Phase: though it is using greedy algorithm, but it waits for unlimited time until it gets a next suitable neighbor.
Tradeoff during Lock Phase between new route calculation and moving on pre-calculated route.

## Slide 30: Delivery-Guaranteed Geocast in MANETs by using ZHLS
Wang-Cheol Song, Hanan Lutfiyya

## Slide 31
Divides network into 2 overlapping zones:
  Zone level topology (with Zone LSPs)
  Node level topology (with Node LSPs)
Zone LSP: has intra-zone and inter-zone routing tables
Node LSP: has identifiers of
  nodes in the same zone, and
  Zone identifiers of neighbors in different zones (Gateway nodes)

## Slide 32: Assumptions
Zone level topology is relatively stable minimizing the effect of mobility
Low simulation velocities, hence considered low mobility of nodes.

## Slide 33: Routing
Gateway nodes send Zone LSPs to sender
Sender evaluates zone topology in the region
Sender determines 1 Zone in each island to send the to receive the packets, and unicasts packet to respective gateway nodes
Packets received are geocasted in the same region

## Slide 35: Weakness
Not considered the case for nodes with high mobility

## Slide 36: Strength
Message delivery guarantee with very high delivery ratio

## Slide 37: geoDTN: Geographic Routing in Disruption Tolerant Networks
Jo Agila Bitsch Link, Daniel Schmitz,
Klaus Wehrle

## Slide 38
Decision based on:
  Previous node movements
  Probabilistic node meeting heuristic
Mobility vector
  Contains all information required for routing decision
  Cluster, Confidence
Neighbor score

## Slide 39: Terminologies used:
Clusters: a bivariate normal distribution function collection containing location of observed nodes
Confidence (of a cluster): exponential decay function provides kind of guarantee of vector
Neighbor Score: value depends on the frequency with which 2 nodes are in radio range at common location

## Slide 40: Routing: Mobility Vectors
Vectors of contacting nodes and their 2-hop neighbors exchanged
ni
nk
vnj, vnk
nj

## Slide 41: Routing: Mobility Vector Updates
ni receives vnj
  ni updates its vectors according to the confidence values
ni receives vnk which it already has
  Update the vector with cluster with high confidence value
ni receives vnk which it does not have yet
  Complete vector adopted

## Slide 42: Routing Modes
  Distance Mode
  Scoring Mode: when node is in vicinity of destination
  Rescue Mode: if message is stuck in local minimum

## Slide 43: Routing Procedure
Whenever a node comes in radio range, message transfer through the node with higher score is chosen
If the score is below threshold, other modes are employed

## Slide 44: Distance Mode
Hill climbing strategy used
Distance of a node to the destination is calculated in terms of confidence and probability

## Slide 45: Rescue Mode
Hill climbing strategy may result in message bundle getting stuck in local minimum
Random walks used a solution

## Slide 46: Scoring Mode
Used when bundle reaches vicinity of destination
Calculation of neighbor scores own neighbor scores with those of the neighborhood. Best score neighbor used to transfer the bundle

## Slide 49: Strengths
Paper takes care of fairness among nodes and also energy efficiency while comparing with other existing routing methods.
Various aspects affecting routing decision (like confidence, cluster formation, scoring) are effectively chosen.
Tested for real world traces.

## Slide 50: Thank You!!